## Slide 1: A BLE-based multi-gateway network infrastructure with handover support for mobile BLE peripherals
SPEAKER : Jia-Wei Guo
ADVISOR: DR. HO-TING WU

## Slide 2: Outline
Introduction
Primer on BLE and BLE over IPv6
Related work
A BLE-based multi-Gateway network infrastructure
Handover approaches
Implementation details
Evaluation
Conclusion
References

## Slide 3: Introduction

## Slide 4: Primer on BLE and BLE over IPv6
Bluetooth Low Energy (BLE) was released in 2011 as part of the Classic Bluetooth specification and both technologies have coexisted and evolved independently since then.
BLE operates in the 2.4 GHz band, utilizing frequencies between 2402 and 2480MHz. The used spectrum is divided into 40 channels, each employing a space of 2 MHz. These channels are divided into 3 primary advertisement channels and 37 connection-oriented channels.
BLE supports two different ways of communication : an advertising mode and a connection-oriented mode.

## Slide 5: Primer on BLE and BLE over IPv6(cont’d)

## Slide 6: Primer on BLE and BLE over IPv6(cont’d)

## Slide 7: Related work

## Slide 8: Implementation details
The BLE peripheral’s role is enacted using a nRF52840 board and the other roles are enacted using Raspberry PI’s.
nRF52840 board is capable of implementing a complete BLE v5.0 supported stack as well as the IPv6 over BLE stack adjustment.
Use official Linux Bluetooth protocol stack(BLueZ) on Raspberry Pi.
To emulate a mobile BLE peripheral performing a handover from one gateway to another gateway, in a controller manner, a manual attenuator is used.

## Slide 9: Implementation details(cont’d)

## Slide 10: Evaluation
The performance of the handover process is predominantly impacted by two steps: disconnecting from the current GW and setting up a connection with the alternative GW.

## Slide 11: Evaluation : passive handover
About disconnecting from current GW
The supervision timeout should not be too low , to avoid unnecessary triggering of the handover procedure.
However , a too high supervision timeout can have a significant impact on the handover latency.
According to the BLE standard, Supervision timeout should be larger than
Notes: Paper的公式是錯的。

## Slide 12: Evaluation : passive handover(cont’d)
About setting up a connection with the alternative GW
Once the BLE peripheral’s supervision timeout has timed out, it transitions back to the advertising state, broadcasting connectable advertisements at a certain advertising interval.
A GW that is not in a connection or still has room for another BLE connection, is in the initiating state and attempts to set up a connection upon receiving the connectable advertisements from the BLE peripheral.

## Slide 13: Evaluation : passive handover(cont’d)
About BLE parameter combinations
The advertising interval should be smaller or equal to the scan window, because otherwise it cannot be guaranteed that the GW will be able to receive a connectable advertisement in an acceptable time window.
A higher scan duty cycle ( scan window/scan interval ) has a positive impact on the handover latency but a negative impact on the energy consumption of the GW.
Notes: 但使用連續scan可降低外圍設備的功耗，因為可較快接收到advertising。

## Slide 14: Evaluation : passive handover(cont’d)

## Slide 15: Evaluation : passive handover(cont’d)

## Slide 16: Evaluation : active handover
About disconnecting from current GW
the current GW will receive a disconnection message from the controller once a roaming decision has made.
After receiving this message, the GW immediately attempts to send a disconnection request to the BLE peripheral.
Upon receiving this request, the peripheral answers with a disconnection acknowledgment.

## Slide 17: Evaluation : active handover(cont’d)
About Setting up a connection with the alternative GW
Once the disconnection has been finalized, the BLE peripheral switches from a connection/advertising state to solely an advertising state, broadcasting connectable advertisements.
In the meantime, the alternative GW has received a connect message from the controller and has switched from nonconnectable to connectable scanning, specifically for the MAC address of the BLE peripheral at hand.
From this point, the handover process is similar to passive handover.

## Slide 18: Evaluation : active handover(cont’d)
Potential Optimizations
The BLE peripheral constantly needs to advertise , This increases energy consumption and decreases the quality of the BLE connection as well.
A possible improvement could employ a proactive decision on when to start and stop advertising. The peripheral can monitor the quality of the current connection (i.e. via RSSI) and decide via these indicators whether it is necessary to advertise its presence or not.

## Slide 19: Evaluation : active handover(cont’d)

## Slide 20: Evaluation : active handover(cont’d)
Notes: Disconnection要先傳資料給外圍設備通知他斷線。

## Slide 21: Evaluation(cont’d)
During a handover process, the BLE peripheral is not reachable from application servers. This implies possible data loss.
The newest BLE standard allows a BLE peripheral to be in a connection with multiple BLE centrals at once.
Allowing the current GW to keep its connection with the BLE peripheral, until the new connection with the alternative GW is established.

## Slide 22: Evaluation(cont’d)
Finally, to avoid constant switching between connectable and non-connectable scanning, two separate BLE modules could be used on the same GW.
One module is in charge of connectable scanning and maintains existing BLE connections.
The other module performs only non-connectable scanning, continuously sending RSSI log messages to the controller.

## Slide 23: Conclusion
In this paper, two architectures are proposed to realize a BLE-based multi-GW network infrastructure that is able to provide bidirectional connectivity to mobile BLE peripherals.
The IP based architecture offers seamless end-to-end IP connectivity between a mobile BLE peripheral and an existing IP network. It limits custom implementation needs, but requires more resources from the already constrained mobile BLE peripheral.

## Slide 24: Conclusion(cont’d)
The non-IP based architecture requires less resources from the BLE peripheral as it employs native BLE communication towards the IoT gateway. However, custom implementation needs are much higher, as a dedicated controller is introduced within the existing network that needs to maintain the state of the infrastructure and the currently associated mobile BLE devices.

## Slide 25: Conclusion(cont’d)
Next to this, two approaches are considered to perform handover within these solutions.
The passive handover approach does not need any extra implementation, but the handover latency can become quite high and a bad BLE connection is still maintained even if a better alternative GW is avail-able nearby.

## Slide 26: Conclusion(cont’d)
Active handover offers a solution by proactively terminating a bad connection when a better alternative GW is available. As such, it can limit the handover latency. Asa downside, this approach requires more extensive custom implementation, implies a higher energy consumption and can limit the available throughput.

## Slide 27: References
Mathias Baert, Pieterjan Camerlynck, Pieter Crombez, Jeroen Hoebeke, “A BLE-Based Multi-Gateway Network Infrastructure with Handover Support for Mobile BLE Peripherals” in IEEE Internatonal Conference on Mobile Adhoc and Sensor Systems (IEEE MASS 2019) , DOI: 10.1109/MASS.2019.00020
M. Nikodem, M. Bawiec, “Experimental Evaluation of Advertisement-Based Bluetooth Low Energy Communication”, MDPI Sensors 2020, DOI:10.3390/s20010107