## Slide 1: A BLE-based multi-gateway network infrastructure with handover support for mobile BLE peripherals
SPEAKER : Jia-Wei Guo
ADVISOR: DR. HO-TING WU

## Slide 2: Outline
Introduction
Primer on BLE and BLE over IPv6
Related work
A BLE-based multi-Gateway network infrastructure
Handover approaches
Implementation details
Evaluation
Conclusion and future work
References

## Slide 3: Introduction

## Slide 4: Primer on BLE and BLE over IPv6
Bluetooth Low Energy (BLE) was released in 2011 as part of the Classic Bluetooth specification and both technologies have coexisted and evolved independently since then.
BLE operates in the 2.4 GHz band, utilizing frequencies between 2402 and 2480MHz. The used spectrum is divided into 40 channels, each employing a space of 2 MHz. These channels are divided into3 primary advertisement channels and 37 connection-oriented channels.
BLE supports two different ways of communication : an advertising mode and a connection-oriented mode.

## Slide 5: Primer on BLE and BLE over IPv6(cont’d)

## Slide 6: Conclusion
In this paper, two architectures are proposed to realize a BLE-based multi-GW network infrastructure that is able to provide bidirectional connectivity to mobile BLE peripherals.
The IP based architecture offers seamless end-to-end IP connectivity between a mobile BLE peripheral and an existing IP network. It limits custom implementation needs, but requires more resources from the already constrained mobile BLE peripheral.

## Slide 7: Conclusion(cont’d)
The non-IP based architecture requires less resources from the BLE peripheral as it employs native BLE communication towards the IoT gateway. However, custom implementation needs are much higher, as a dedicated controller is introduced within the existing network that needs to maintain the state of the infrastructure and the currently associated mobile BLE devices.

## Slide 8: Conclusion(cont’d)
Next to this, two approaches are considered to perform handover within these solutions.
The passive handover approach does not need any extra implementation, but the handover latency can become quite high and a bad BLE connection is still maintained even if a better alternative GW is avail-able nearby.

## Slide 9: Conclusion(cont’d)
Active handover offers a solution by proactively terminating a bad connection when a better alternative GW is available. As such, it can limit the handover latency. Asa downside, this approach requires more extensive custom implementation, implies a higher energy consumption and can limit the available throughput.

## Slide 10: References
Mathias Baert, Pieterjan Camerlynck, Pieter Crombez, Jeroen Hoebeke, “A BLE-Based Multi-Gateway Network Infrastructure with Handover Support for Mobile BLE Peripherals” in IEEE Internatonal Conference on Mobile Adhoc and Sensor Systems (IEEE MASS 2019) , DOI: 10.1109/MASS.2019.00020
M. Nikodem, M. Bawiec, “Experimental Evaluation of Advertisement-Based Bluetooth Low Energy Communication”, MDPI Sensors 2020, DOI:10.3390/s20010107